Detailed Changes to Arduino Code

Code Review:
The Arduino code is well-structured and uses appropriate libraries for sensor integration and motor control, implement a basic obstacle avoidance system using an ultrasonic sensor.

//HEADER FILES// / #define USE_USBCON / #include <Wire.h> / #include <PID_v1.h> / #include <ros.h> / #include <std_msgs/String.h> / #include <geometry_msgs/Vector3Stamped.h> / #include <geometry_msgs/Twist.h> / #include <geometry_msgs/Pose2D.h> / #include <ros/time.h> / #include <ArduinoHardware.h> / #include <std_msgs/Float64.h> / #include <Adafruit_BNO055.h> / #include <utility/imumaths.h> / #include <tf/transform_broadcaster.h> / #include <sensor_msgs/Imu.h> / #include <sensor_msgs/Range.h> / #include <std_msgs/Bool.h> / #include <Ultrasonic.h> / #include <LedControl.h> / //PINS DECLERATION// / #define dir_rig 8 / #define pwm_rig 6 / #define dir_lef 9 / #define pwm_lef 7 / #define INTERRUPT_PIN_RAIS_A_RIG 31 / #define INTERRUPT_PIN_RAIS_B_RIG 35 / #define INTERRUPT_PIN_RAIS_A_LEF 22 / #define INTERRUPT_PIN_RAIS_B_LEF 24 / #define TRIG 11 / #define ECHO 12 / #define button_pin 5 / #define led_pin 13 / #define DIN 2 / #define CS 3 / #define CLK 4 / LedControl lc = LedControl(DIN, CLK, CS, 8); / unsigned long currentTime; / unsigned long lastUpdateTime = 0; / const long eyesDelay = 500; / const long emptyDelay = 500; / byte eyesPatterns[8][8] = { / {0x00, 0x00, 0xC0, 0xF0, 0xF8, 0xF8, 0xFC, 0xFC}, / {0x00, 0x00, 0x03, 0x0F, 0x1F, 0x1F, 0x33, 0x31}, / {0x00, 0x00, 0xC0, 0xF0, 0xF8, 0xF8, 0xCC, 0x8C}, / {0x00, 0x00, 0x03, 0x0F, 0x1F, 0x1F, 0x3F, 0x3F}, / {0x00, 0x00, 0xC0, 0xF0, 0xF8, 0xF8, 0xFC, 0xFC}, / {0x00, 0x00, 0x03, 0x0F, 0x1F, 0x1F, 0x33, 0x39}, / {0x00, 0x00, 0xC0, 0xF0, 0xF8, 0xF8, 0xCC, 0x9C}, / {0x00, 0x00, 0x03, 0x0F, 0x1F, 0x1F, 0x3F, 0x3F} / }; / byte emptyPattern[8] = {0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00}; / //VARIABLE DECLERATIONS// / #define LOOPTIME 100 // Looptime in milliseconds / const byte noCommLoopMax = 10; // Max loops without communication before stopping / unsigned int noCommLoops = 0; // Counter for loops without communication / Adafruit_BNO055 bno = Adafruit_BNO055(55, 0x28); / bool last_reading; / long last_debounce_time = 0; / long debounce_delay = 6000; / bool published = true; / Ultrasonic ultrasonic_m(TRIG, ECHO); / long ultra_last_debounce_time = 0; / long ultra_debounce_delay = 60000; / int duration; / int distance; / int ultracount; / int u_m; / volatile byte state = LOW; / signed long int count_rig = 0, count_lef = 0; / int en_a_state_rig = 0, en_b_state_rig = 0, en_a_las_state_rig = 0, en_b_las_state_rig = 0; / int en_a_state_lef = 0, en_b_state_lef = 0, en_a_las_state_lef = 0, en_b_las_state_lef = 0; / long encoder_left = 0; / long encoder_right = 0; / const double speed_pwm = 0.00148; // DC motors / const double min_speed_cmd = 0.02962; // 100 RPM / unsigned long lastMilli = 0, lm = 0; / const double radius = 0.0625; // Wheel radius in meters / const double wheelbase = 0.32; // Wheelbase in meters / double c_r = 0, c_l = 0; / double speed_req = 0; // Desired linear speed for the robot in m/s / double angular_speed_req = 0; // Desired angular speed in rad/s / double speed_req_left = 0; // Desired speed for left wheel in m/s / double speed_act_left = 0; // Actual speed for left wheel in m/s / double speed_cmd_left = 0; // Commanded speed for left wheel in m/s / double speed_req_right = 0; // Desired speed for right wheel in m/s / double speed_act_right = 0; // Actual speed for right wheel in m/s / double speed_cmd_right = 0; // Commanded speed for right wheel in m/s / const double max_speed = 0.03599; // Max speed in m/s / //Initialize PWM values to zero / int PWM_leftMotor = 0; / int PWM_rightMotor = 0; / int d = 0; / const double PID_left_param[] = {0.24, 0, 1}; // Kp, Ki, Kd for left motor PID / const double PID_right_param[] = {0.24, 0, 1}; // Kp, Ki, Kd for right motor PID / PID PID_leftMotor(&speed_act_left, &speed_cmd_left, &speed_req_left, / PID_left_param[0], PID_left_param[1], PID_left_param[2], DIRECT); / PID PID_rightMotor(&speed_act_right, &speed_cmd_right, &speed_req_right, / PID_right_param[0], PID_right_param[1], PID_right_param[2], DIRECT); / ros::NodeHandle nh; / /************************************************************************************** / Function to Handle cmd_vel / **************************************************************************************/ / void handle_cmd(const geometry_msgs::Twist& cmd_vel) { / noCommLoops = 0; // Reset the counter for number of loops without communication / speed_req = cmd_vel.linear.x; // Extract the commanded linear speed / angular_speed_req = cmd_vel.angular.z; // Extract the commanded angular speed / speed_req_left = speed_req - angular_speed_req * (wheelbase / 2); // Calculate left motor speed / speed_req_right = speed_req + angular_speed_req * (wheelbase / 2); // Calculate right motor speed / } / //Declaration of PUB & SUB Message Types / geometry_msgs::Pose2D pwm_output_msg; / geometry_msgs::Pose2D encoder_msg; / geometry_msgs::Vector3Stamped speed_msg; / sensor_msgs::Imu imu_msg; / sensor_msgs::Range sonar_msg_m; // Ultrasonic / std_msgs::Bool pushed_msg; / geometry_msgs::TransformStamped t; / geometry_msgs::TransformStamped l; / tf::TransformBroadcaster broadcaster; / char base_link[] = "/base_link"; / char imu_frame[] = "/imu"; / char ultra_frame[] = "/ultrasonic"; / ros::Publisher pub_sonar_m("rangeSonar", &sonar_msg_m); / ros::Publisher pub_button("pushed", &pushed_msg); / ros::Publisher imu_pub("imu_data", &imu_msg); / ros::Subscriber<geometry_msgs::Twist> cmd_vel("cmd_vel", handle_cmd); / ros::Publisher speed_pub("speed", &speed_msg); / ros::Publisher pwm_output_pub("pwm_output", &pwm_output_msg); / ros::Publisher encoder_pub("encoder", &encoder_msg); / /************************************************************************************************ / SETUP FUNCTION / ************************************************************************************************/ / void setup() / { / for (int i = 0; i < 8; i++) / { / lc.shutdown(i, false); / lc.setIntensity(i, 5); / lc.clearDisplay(i); / } / // Initialize ROS node / nh.initNode(); / // Set baud rate for ROS serial communication / nh.getHardware()->setBaud(115200); / // Subscribe to ROS topic for velocity commands / nh.subscribe(cmd_vel); / // Prepare to publish speed in ROS topics / nh.advertise(speed_pub); / nh.advertise(encoder_pub); / nh.advertise(pwm_output_pub); / nh.advertise(imu_pub); / nh.advertise(pub_button); / nh.advertise(pub_sonar_m); / // Initialize broadcaster for ROS / broadcaster.init(nh); / ultrasonic_m.setTimeout(40000UL); / // Configure pins for LEDs and button / pinMode(led_pin, OUTPUT); / pinMode(button_pin, INPUT); / // Enable the pull-up resistor on the button / digitalWrite(button_pin, HIGH); / while (!bno.begin()) / { / nh.loginfo("No BNO055 detected"); / } / // Set up motor control pins / pinMode(pwm_rig, OUTPUT); / pinMode(dir_rig, OUTPUT); / pinMode(pwm_lef, OUTPUT); / pinMode(dir_lef, OUTPUT); / // Set up interrupt pins for right motor encoders / pinMode(INTERRUPT_PIN_RAIS_A_RIG, INPUT_PULLUP); / attachInterrupt(digitalPinToInterrupt(INTERRUPT_PIN_RAIS_A_RIG), rais_a_rig, CHANGE); // Change Interrupt state to RISING to CHANGE State / pinMode(INTERRUPT_PIN_RAIS_B_RIG, INPUT_PULLUP); / attachInterrupt(digitalPinToInterrupt(INTERRUPT_PIN_RAIS_B_RIG), rais_b_rig, CHANGE); // Change Interrupt state to RISING to CHANGE State / // Set up interrupt pins for left motor encoders / pinMode(INTERRUPT_PIN_RAIS_A_LEF, INPUT_PULLUP); / attachInterrupt(digitalPinToInterrupt(INTERRUPT_PIN_RAIS_A_LEF), rais_a_lef, CHANGE); // Change Interrupt state to RISING to CHANGE State / pinMode(INTERRUPT_PIN_RAIS_B_LEF, INPUT_PULLUP); / attachInterrupt(digitalPinToInterrupt(INTERRUPT_PIN_RAIS_B_LEF), rais_b_lef, CHANGE); // Change Interrupt state to RISING to CHANGE State / } / /************************************************************************************************ / LOOP FUNCTION / ************************************************************************************************/ / void loop() / { / currentTime = millis(); / // Determine if we should show the eyes or empty pattern / if (currentTime - lastUpdateTime >= eyesDelay && (currentTime - lastUpdateTime) < (eyesDelay + emptyDelay)) { / showEyes(); / } else if (currentTime - lastUpdateTime >= (eyesDelay + emptyDelay)) { / showEmpty(); / lastUpdateTime = currentTime; // Reset lastUpdateTime after displaying empty state / } / nh.spinOnce(); / if ((millis() - lastMilli) >= LOOPTIME) { / lastMilli = millis(); / // Read and calculate speeds / c_l = count_lef; / c_r = count_rig; / if (abs(count_lef) < 5) { / speed_act_left = 0; // Ignore minor disturbances / } else { / speed_act_left = ((c_l / 2800.0) * 2 * (22 / 7.0) * radius) * (1000.0 / LOOPTIME); // Change the tick value 2786 to 2800 / } / if (abs(count_rig) < 5) { / speed_act_right = 0; // Ignore minor disturbances / } else { / speed_act_right = ((c_r / 2800.0) * 2 * (22 / 7.0) * radius) * (1000.0 / LOOPTIME); // Change the tick value 2786 to 2800 / } / encoder_left += count_lef; / encoder_right += count_rig; / // Reset encoder counts / count_lef = 0; / count_rig = 0; / // Left Motor Control / speed_cmd_left = constrain(speed_cmd_left, -max_speed, max_speed); / PID_leftMotor.Compute(); // Compute PWM for left motor / PWM_leftMotor = constrain( / ((speed_req_left + sgn(speed_req_left) * min_speed_cmd) / speed_pwm) + / (speed_cmd_left / speed_pwm), / -255, 255 / ); / if (noCommLoops >= noCommLoopMax) { / analogWrite(pwm_lef, 0); // Stop motor if communication timeout / } else if (speed_req_left == 0) { / analogWrite(pwm_lef, 0); // Stop motor if no speed request / } else if (PWM_leftMotor > 0) { / analogWrite(pwm_lef, PWM_leftMotor); // Move forward / digitalWrite(dir_lef, HIGH); / } else { / analogWrite(pwm_lef, abs(PWM_leftMotor)); // Move backward / digitalWrite(dir_lef, LOW); / } / // Right Motor Control / speed_cmd_right = constrain(speed_cmd_right, -max_speed, max_speed); / PID_rightMotor.Compute(); // Compute PWM for right motor / PWM_rightMotor = constrain( / ((speed_req_right + sgn(speed_req_right) * min_speed_cmd) / speed_pwm) + / (speed_cmd_right / speed_pwm), / -255, 255 / ); / if (noCommLoops >= noCommLoopMax) { / analogWrite(pwm_rig, 0); // Stop motor if communication timeout / } else if (speed_req_right == 0) { / analogWrite(pwm_rig, 0); // Stop motor if no speed request / } else if (PWM_rightMotor > 0) { / analogWrite(pwm_rig, PWM_rightMotor); // Move forward / digitalWrite(dir_rig, HIGH); / } else { / analogWrite(pwm_rig, abs(PWM_rightMotor)); // Move backward / digitalWrite(dir_rig, LOW); / } / // Increment communication loops counter / noCommLoops++; / if (noCommLoops == 65535) { / noCommLoops = noCommLoopMax; // Prevent overflow / } / // Sensor updates and data publishing / updateimu(); / publishSpeed(); / updateexit(); / updateultra(); / } / } / /******************************************************************************************** / Publish speed function / *********************************************************************************************/ / void publishSpeed() { / // Update speed message / speed_msg.header.stamp = nh.now(); // Timestamp for odometry data / speed_msg.vector.x = speed_act_left; // Left wheel speed (m/s) / speed_msg.vector.y = speed_act_right; // Right wheel speed (m/s) / speed_msg.vector.z = 0.1; // Loop time (should match LOOPTIME in seconds) / speed_pub.publish(&speed_msg); / // Update encoder message / encoder_msg.x = millis(); // Current timestamp in milliseconds / encoder_msg.y = encoder_right; // Right wheel encoder count / encoder_pub.publish(&encoder_msg); / // Update PWM output message / pwm_output_msg.x = PWM_leftMotor; // PWM value for left motor / pwm_output_msg.y = PWM_rightMotor; // PWM value for right motor / pwm_output_pub.publish(&pwm_output_msg); / // Publish IMU data / imu_pub.publish(&imu_msg); / // Trigger ROS communication / nh.spinOnce(); / // Optional log for debugging (can be disabled in production) / nh.loginfo("Odometry data published"); / } / /************************************************************************************** / update imu / **************************************************************************************/ / void updateimu() { / nh.spinOnce(); / imu::Quaternion quat = bno.getQuat(); / sensors_event_t orientationData , angVelocityData , linearAccelData, magnetometerData, accelerometerData, gravityData; / bno.getEvent(&angVelocityData, Adafruit_BNO055::VECTOR_GYROSCOPE); / bno.getEvent(&accelerometerData, Adafruit_BNO055::VECTOR_ACCELEROMETER); / imu_msg.header.stamp = nh.now(); / imu_msg.header.frame_id = "imu"; / imu_msg.orientation.x = quat.x(); / imu_msg.orientation.y = quat.y(); / imu_msg.orientation.z = quat.z(); / imu_msg.orientation.w = quat.w(); / imu_msg.angular_velocity.x = angVelocityData.gyro.x; / imu_msg.angular_velocity.y = angVelocityData.gyro.y; / imu_msg.angular_velocity.z = angVelocityData.gyro.z; / imu_msg.linear_acceleration.x = accelerometerData.acceleration.x; / imu_msg.linear_acceleration.y = accelerometerData.acceleration.y; / imu_msg.linear_acceleration.z = accelerometerData.acceleration.z; / l.header.frame_id = base_link; / l.child_frame_id = imu_frame; / l.transform.rotation.x = 0; / l.transform.rotation.y = 0; / l.transform.rotation.z = 0; / l.transform.rotation.w = 1.0; / l.header.stamp = nh.now(); / { lm = millis(); / broadcaster.sendTransform(l); / } / } / /************************************************************************************** / Button Update / **************************************************************************************/ / void updateexit() / { / bool reading = digitalRead(button_pin); / if (reading == 0 && (millis() - last_debounce_time) > debounce_delay) { // Using logical operator to optimize if condition / last_debounce_time = millis(); / pushed_msg.data = reading; / pub_button.publish(&pushed_msg); / nh.loginfo("0"); / } / } / /************************************************************************************** / Ultrasonic Sensor Update / **************************************************************************************/ / void updateultra() / { / // Read ultrasonic distance / u_m = ultrasonic_m.read(); // optimize u_m data from multiple initializtion and update in if condition / // Check if the distance is less than 200 / if (u_m < 200) { / ultracount = 0; / if ((millis() - ultra_last_debounce_time) > ultra_debounce_delay) { / ultra_last_debounce_time = millis(); / sonar_msg_m.range = u_m; / pub_sonar_m.publish(&sonar_msg_m); / nh.loginfo("ultrasonic"); / } / } else { / ultracount = 1; / } / } / /************************************************************************************** / Encoder Calculations for Right Motor / **************************************************************************************/ / void rais_a_rig(){ / en_a_state_rig = digitalRead(INTERRUPT_PIN_RAIS_A_RIG); // use digitalRead to read sensor value / calculataion_rig(); / } / void rais_b_rig() { / en_b_state_rig = digitalRead(INTERRUPT_PIN_RAIS_B_RIG); // use digitalRead to read sensor value / calculataion_rig(); / } / void calculataion_rig() { // create a function using comparision operator / if (en_a_state_rig != en_a_las_state_rig) { / count_rig += (en_b_state_rig == en_a_state_rig) ? -1 : 1; / } else if (en_a_state_rig == en_a_las_state_rig) { / if (en_b_state_rig != en_b_las_state_rig) { / count_rig += (en_b_state_rig != en_a_state_rig) ? -1 : 1; // implace of using unary opertor use binary operator / } / } / en_a_las_state_rig = en_a_state_rig; / en_b_las_state_rig = en_b_state_rig; / } / /************************************************************************************** / Encoder Calculations for Left Motor / **************************************************************************************/ / void rais_a_lef() { / en_a_state_lef = digitalRead(INTERRUPT_PIN_RAIS_A_LEF); // use digitRead to reading encoder value to high / calculataion_lef(); / } / void rais_b_lef() { / en_b_state_lef = digitalRead(INTERRUPT_PIN_RAIS_B_LEF); // use digitRead to reading encoder value to high / calculataion_lef(); / } / void calculataion_lef() { // create a function using comparision operator / if (en_a_state_lef != en_a_las_state_lef) { / count_lef += (en_b_state_lef == en_a_state_lef) ? 1 : -1; / } else if (en_a_state_lef == en_a_las_state_lef) { / if (en_b_state_lef != en_b_las_state_lef) { / count_lef += (en_b_state_lef != en_a_state_lef) ? 1 : -1; // implace of using unary opertor use binary operator / } / } / en_a_las_state_lef = en_a_state_lef; / en_b_las_state_lef = en_b_state_lef; / } / /************************************************************************************** / Stop Motors / **************************************************************************************/ / void dc_stop() { / Serial.println("stopped"); / analogWrite(pwm_rig, 0); / analogWrite(pwm_lef, 0); / digitalWrite(dir_rig, LOW); / digitalWrite(dir_lef, HIGH); / } / /************************************************************************************** / Sign Function / **************************************************************************************/ / template <typename T> int sgn(T val) { / return (T(0) < val) - (val < T(0)); / } / /************************************************************************************** / Eyes Pattern Function / **************************************************************************************/ / void showEyes() / { / for (int i = 0; i < 8; i++) / { / for (int row = 0; row < 8; row++) / { / lc.setRow(i, row, eyesPatterns[i][row]); / } / } / } / /************************************************************************************** / Eyes Blink Display Function / **************************************************************************************/ / void showEmpty() / { / for (int i = 0; i < 8; i++) / { / for (int row = 0; row < 8; row++) / { / lc.setRow(i, row, emptyPattern[row]); / } / } / }

Key Changes and Analysis:

1. Ultrasonic Sensor:
   - Integrated an ultrasonic sensor using the `Ultrasonic` library. The `updateultra()` function reads the distance and publishes it on the `rangeSonar` topic.

2. Encoder Inputs:
   - Changed the encoder input configuration to use two separate pins for each encoder (A and B phases). This allows for more accurate quadrature encoding and direction determination.

3. Motor Control:
- The motor control logic is based on PID controllers for each wheel. The `handle_cmd` function receives velocity commands from the `cmd_vel` topic and calculates the required wheel speeds.
   - The `loop()` function reads encoder values, calculates actual wheel speeds, and computes PWM values for the motors using the PID controllers.

4. IMU Integration:
   - Integrated a BNO055 IMU sensor. The `updateimu()` function reads orientation and angular velocity data from the IMU and publishes it on the `imu_data` topic. It also publishes a transform between the base_link and imu frames.

5. Button Input:
   - Implemented a button input. The `updateexit()` function detects button presses and publishes a boolean message on the `pushed` topic.

6. LED Control (Eyes):
   - Added code to control LEDs in an "eyes" pattern. This is likely for visual feedback or aesthetics.

Potential Issues and Improvements:

- PID Tuning: The PID parameters might need to be tuned for optimal performance.

- Encoder Resolution:The encoder resolution (2800 ticks) seems a bit low. Higher resolution encoders would provide more precise speed control.

- Motor Control Logic: The motor control logic could be improved by adding features like current limiting and stall detection.

- Ultrasonic Sensor Noise: Ultrasonic sensors can be noisy. Consider adding filtering or averaging to the distance readings.

-Code Structure: The code could be better organized by separating the different functionalities into separate functions or classes.

Hardware Connection:
1. 1st Encoder connected to Arduino Due connected A to 31 and B to 35.
2. 2nd Encoders connected to Arduino Due connected A to 22 and B to 24.
3. Ultrasonic Sensor : Ultrasonic Sensor trig pin connected to pin 11 of arduino due and echo pin connected to pin 12 of arduino due. GND to GND. VCC to arduino Due of 5V.
    1. VCC → 5V pin on Arduino Due
    2. GND → GND pin on Arduino Due
    3. Trig → Digital Pin (specified in Arduino code)
    4. Echo → Digital Pin (specified in Arduino code).

Update Block Diagram: