AUTONOMOUS BOT

Components List:
- Arduino Due
- Raspberry Pi-4
- DC Motor
- MDD10A Motor Driver
- Raspberry Pi-3
- YD -Lidar
- BNO055 Sensor
- Exit Sensor
- Buck Converter(LM2596)
- Led stripes
- Switch
- 24V Battery
- Encoders(OE-28/OE-37)
- USB Connector
- Chest Display
- Sound Card
- Audio Jack
- PAM
- woofer
- Connector (XT-60, SB-50)

ARDUINO DUE

Microcontroller	AT91SAM3X8E
Operating Voltage	3.3V
Input Voltage (recommended)	7-12V
Input Voltage (limits)	6-16V
Digital I/O Pins	54 (of which 12 provide PWM output)
Analog Input Pins	12
Analog Output Pins	2 (DAC)
Total DC Output Current on all I/O lines	130 mA
DC Current for 3.3V Pin	800 mA
DC Current for 5V Pin	800 mA
Flash Memory	512 KB all available for the user applications
SRAM	96 KB (two banks: 64KB and 32KB)
Clock Speed	84 MHz
Length	101.52 mm
Width	53.3 mm
Weight	36 g

The Arduino Due is a microcontroller board based on the Atmel SAM3X8E ARM Cortex-M3 CPU. It is the first Arduino board based on a 32-bit ARM core microcontroller. It has 54 digital input/output pins (of which 12 can be used as PWM outputs), 12 analog inputs, 4 UARTs (hardware serial ports), a 84 MHz clock, an USB OTG capable connection, 2 DAC (digital to analog), 2 TWI, a power jack, an SPI header, a JTAG header, a reset button and an erase button.

Arduino Due is used for real-time control of motors and sensors because microcontrollers are faster for these tasks.
Purpose:
- Real-time motor and sensor control tasks, which are faster on microcontrollers.
- Interfaces with the Motor Driver using PWM and direction pins.
- Communicates with sensors like the BNO055 and encoders.

Raspberry Pi-4

Specification: More advanced single-board computer with better processing power than Pi 3.
Purpose:
- Handles tasks requiring higher processing, such as:
  - LIDAR Sensor Data for real-time mapping and obstacle detection.
  - Audio Processing through the sound card and audio output system.

DC Motor
### Left and Right DC Motors
- Specification: High-torque DC motors with encoders.
- Purpose: Provides the bot’s propulsion (forward, backward, and turning).
- Encoders: Attached to the motors to provide feedback on:
  - Position: Tracks wheel rotation for distance measurement.
  - Speed: Enables precise control of motor speed.

MDD10A Motor Driver
The Motor Driver acts as an interface between the Arduino Due and the DC motor.
- The Arduino Due sends control signals to the motor driver, which then regulates the voltage and current supplied to the motor.
- The motor driver allows:
  - Speed Control using PWM (Pulse Width Modulation).
  - Direction Control using Direction Pins.
## Connection Diagram
Assume we are using the MDD10A motor driver (as shown in your circuit) for simplicity.
### MDD10A Motor Driver Pins:
1. PWM1 and PWM2: Control the motor speed using PWM signals.
2. DIR1 and DIR2: Control motor direction (HIGH/LOW signal).
3. M1A, M1B: Output pins for Motor 1.
4. M2A, M2B: Output pins for Motor 2.
5. GND and VCC: Power supply connections.
### Steps to Connect the DC Motor with Arduino Due
#### 1. Power Connections
- Connect the VCC of the motor driver to a 12V/24V Power Supply (based on your motor specification).
- Connect the GND of the power supply to the motor driver GND.
- Connect the GND of the motor driver to the GND pin of the Arduino Due to ensure a common ground.
#### 2. Motor Connections
- Connect the DC motor terminals to the motor driver output pins:
  - M1A and M1B → Motor 1 terminals
  - M2A and M2B → Motor 2 terminals (if you are using two motors).
#### 3. Control Connections to Arduino Due
- Connect the PWM pins of the motor driver to Arduino Due PWM-enabled pins (e.g., Pin 7 and Pin 8):
  - PWM1 → Pin 7
  - PWM2 → Pin 8
- Connect the Direction Pins (DIR1 and DIR2) of the motor driver to digital pins on the Arduino Due:
  - DIR1 → Pin 9
  - DIR2 → Pin 10

Raspberry Pi-3
Quad Core 1.2GHz Broadcom BCM2837 64bit CPU
- 1GB RAM
- BCM43438 wireless LAN and Bluetooth Low Energy (BLE) on board
- 100 Base Ethernet
- 40-pin extended GPIO
- 4 USB 2 ports
- 4 Pole stereo output and composite video port
- Full size HDMI
- CSI camera port for connecting a Raspberry Pi camera
- DSI display port for connecting a Raspberry Pi touchscreen display
- Micro SD port for loading your operating system and storing data
- Upgraded switched Micro USB power source up to 2.5A

YDLidar
### YD LIDAR Sensor
- Specification: A 360° LIDAR sensor connected via a Type-C cable.
- Purpose:
  - Scans the environment to detect obstacles and create a 2D/3D map for navigation.
  - Feeds data to Raspberry Pi 4 for real-time processing.
Exit Sensor
Specification: Basic sensor to detect the completion of a task or arrival at a specific endpoint.
Purpose: Acts as a trigger for stopping or transitioning the bot to a new task.
Chest Display
Purpose: Displays system information, such as battery voltage, navigation status, or error messages.
Sound Card
Specification: External sound card connected to Raspberry Pi 4.
Purpose: Processes audio signals for playback.
### PAM (Power Amplifier Module)
Specification: Amplifies audio signals for driving speakers/woofers.
Purpose: Ensures clear and loud audio output.
Woofer
Purpose: Outputs alerts, instructions, or other sound-based feedback.

Connector
### USB Ports
Used to connect peripherals like sensors or provide additional power.
### Type-C Cable
Connects the YD LIDAR Sensor to the Raspberry Pi 4 for power and data transfer.
XT60 Male/Female Connectors
  - Specification: High-current connectors commonly used for batteries.
  - Purpose: Enables secure connections for the 24V battery to the circuit.

BNO055 Sensor
VIN: 3.3-5.0V power supply input
3VO: 3.3V output from the on-board linear voltage regulator, you can grab up to about 50mA as necessary
GND: The common/GND pin for power and logic
SCL - I2C clock pin, connect to your microcontrollers I2C clock line. This pin can be used with 3V or 5V logic, and there's a 10K pullup on this pin.
SDA - I2C data pin, connect to your microcontrollers I2C data line. This pin can be used with 3V or 5V logic, and there's a 10K pullup on this pin.
Default address of the BNO055 device is 0101001b(0x29) and alternate addr is 0x28.
## Purpose of BNO055
1. Absolute Orientation:
  1. The BNO055 combines accelerometer, gyroscope, and magnetometer data internally to provide Euler angles (yaw, pitch, roll) or quaternions.
  2. This removes the need for manual sensor fusion, reducing the processing load on the Raspberry Pi or Arduino Due.
2. Stabilization:
  1. The gyroscope data helps stabilize the bot by detecting tilts, rotations, and angular velocities.
  2. For example, when the bot turns, the BNO055 provides precise rotation angles for smooth and accurate motion control.
3. Navigation:
  1. The magnetometer acts as a digital compass, helping the bot determine its heading (North, South, East, West).
  2. Combined with encoder data, the bot can accurately navigate to its destination.

Buck Converter(LM2596)
Buck converters are DC-to-DC voltage regulators that step down voltage efficiently.To isolate power for different components and avoid overloading a single power source.
5AMP Buck Converter (-12V)
  - Specification: Steps down 24V to 12V, supports a current output of 5A.
  - Purpose: Provides 12V power to medium-voltage devices like the Motor Driver (MDD10A), Chest Display, and sensors.
2AMP Buck Converter (5V)
  - Specification: Steps down 12V/24V to 5V, with a current output of 2A.
  - Purpose: Supplies power to:
    - Raspberry Pi 3 and 4 (primary controllers)
    - USB Ports for peripherals like the LIDAR Sensor and Exit Sensor
    - BNO055 Sensor

24V Battery
- The 24V battery connects to the motor driver’s VCC and GND pins.
- The motor driver then supplies power to the left and right motors.
  The 24V battery is connected to multiple buck converters to provide lower voltages:
- 12V Buck Converter: Powers the MDD10A motor driver and other 12V components like LED displays.
- 5V Buck Converters: Step down to 5V for the Raspberry Pi, sensors, and auxiliary USB ports.
  Encoders(OE-28 Hall Effect Two Channel Magnetic Encoder)
#### Encoder Pinouts:

Pin	Description
VCC	Power supply (+5V)
GND	Ground
CHA	Channel A signal output
CHB	Channel B signal output
M-	Motor negative terminal
M+	Motor positive terminal

The encoder outputs two square wave signals (CHA and CHB) as the motor rotates.
The signals are 90° out of phase:
- If CHA leads CHB, the motor is rotating in one direction (e.g., clockwise).
- If CHB leads CHA, the motor is rotating in the opposite direction (e.g., counterclockwise).